## Slide 1: Assembler Directives
Pseudo-operations
  do not refer to operations executed by program
  used by assembler
  look like instruction, but “opcode” starts with dot
Opcode | Operand | Meaning
.ORIG | address | starting address of program
.END |  | end of program
.BLKW | n | allocate n words of storage
.FILL | n | allocate one word, initialize with value n
.STRINGZ | n-character string | allocate n+1 locations, initialize w/characters and null terminator

## Slide 2: LC-3 TRAP Routines(service routines)
  GETC (TRAP x20)
    Read a single character from KBD.
    ASCII copied in R0, R0[15:8] cleared.
  OUT (TRAP x21)
    Write R0[7:0] to screen.
  PUTS (TRAP x22)
    Write a string to screen. String address in R0.
  IN (TRAP x23)
    Print a prompt on the screen and read a single character from KBD.
    Character is echoed to Display. ASCII copied to R0[7:0] and R0[15:8] cleared.
  HALT (TRAP x25)
    Prints message on screen & halts execution.
:
x0400
x0430
x0450
x04A0
x04E0
xFD70
x0000
:
x0020
x0021
x0022
x0023
x0024
x0025
:
:
x00FF
The LC-3 System
Control Block

## Slide 3: ASCII（American Standard Code for Information Interchange）